## Slide 1: Multicasting in IP Networks
Ravi Prakash

## Slide 2: Objectives
Need for multicasting?
What is multicasting?
Issues.
Internet Group Management Protocol.
Classification of solutions.
Scalability issues.
Protocol descriptions.

## Slide 3: Multicasting Applications
Advertisements by servers.
Server solicitation, by clients.
Audio and video conferencing.
Distributed gaming.
Notes: Multicasting has received considerable attention because it is quite suitable for a variety of applications. For example, a server may wish to advertise its presence to multiple nodes that may be potentially interested in its services. A client, trying to locate a server, may multicast its solicitation message to those parts of the network where it expects to find the server. In audio and video conferencing, each participant wants to send his/her audio and video streams to all other participants. Thus, for each source, there are as many destinations as the number of participants in that conference. Similarly, in distributed gaming, all the players playing the game at a given time should be able to communicate their actions to all other players.

## Slide 4: What is IP Multicasting?
Transmission of a packet to a group of nodes.
All nodes may not be on the same network.
How about the following approaches?
Unicasting to each node in the group.
Broadcasting to all, with nodes responsible for selectively accepting packets destined for their group(s).
Notes: So far we have discussed unicasting in IP networks, where a packet has only one destination. In IP multicasting, each packet has multiple destinations. The set of destinations is denoted by a Class D IP address, also referred to as a group address. As discussed earlier, a Class D address has a prefix of 1110. Thus, there can be up to 228 group addresses. Broadcasting is a special case of multicasting where all nodes in the network are members of the group.
All members of a group need not belong to the same LAN. Instead, they could belong to multiple networks, interconnected to each other by intermediate routers.
The simplest approach to multicasting would be to broadcast the message, either by flooding or some other means, to all nodes in the network. Then, have each node decide whether it should accept the message (if it belongs to the corresponding multicast group) or ignore it. This could be very expensive for two reasons. First, all nodes have to process all multicast packets, even though they may not be members of the multicast group. Second, the message propagates to all parts of the network, including those that do not contain any members of the multicast group. Hence, this incurs high network overheads.
Another approach could be to implement N unicasts for a group of N nodes: one from the source to each group member. This is infeasible for two reasons. First, several unicast paths may overlap, and multiple copies of the message are sent along these overlapping segments, incurring high communication overheads. Second, if the multicast group is large, it may be too much work for the multicast source and the network to keep track of all nodes that belong to the group.
So, it appears that neither of the two approaches is acceptable due to obvious scalability problems. Multicasting in the network is performed by constructing a tree that spans all the group members. Packets multicast to the group are propagated along this tree to reach all the member nodes. The fundamental question is how to construct a multicast tree? In the following slides we will discuss various multicast tree construction approaches.

## Slide 5: Multicasting Issues
How are groups started and terminated?
How is a group IP address chosen?
Are there any restrictions on group membership?
Do group members know identities of each other?
Does the sender have to belong to the group?
How does the network deliver packets to all group members?
Notes: So far we know that the set of recipients of a multicast message are referred as the multicast group. But, how is such a group formed, and how are nodes in a group collectively addressed? Is there a central entity that initiates the formation of a group? Similarly, is there a central entity that assigns a Class D IP address to a group?
Are multicast groups open, i.e., can any node join the multicast group? Or, are there restrictions on joining a group? If there are restrictions, how would one enforce them?
Do all the members of a group know about each other? A related question is whether only members of a group can send messages to each other, or can a non-member also send messages to the group? If a non-member can send messages to the group, does that non-member need to know the composition of the group? Is it scalable to have nodes maintain memberships of groups, as multicasting becomes more popular and group sizes increase?
Finally, how are multicast messages propagated? In the last slide we stated that flooding is not a feasible solution, nor is sending a separate message to each of the group members. So, how multicasting be accomplished in an efficient fashion?

## Slide 6: Internet Group Management Protocol (IGMP)
Runs locally between a node and its attached router.
Used by node to inform the router about desire to join a specific multicast group.
Multicast routing protocol coordinates between the routers.
R
R
R
Wide Area
Multicast
Routing
Notes: The Internet Group Management Protocol (IGMP) is used by nodes to inform their associated routers about their group membership(s). No single entity in the network knows the full membership of a multicast group. All a multicast-enabled router knows is which nodes in its attached network belong to a particular multicast group. These routers do not communicate their membership lists to other routers. At most, a router may tell other routers whether there is at least one node in its attached network that belongs to a given group. A multicast routing protocol uses such information exchange between routers to determine how packets addressed to a multicast group should be forwarded.
In this figure we have three LANs. In the LANs to the left and above the wide area multicast network only one node belongs to a multicast group. In the LAN to the right, both the nodes belong to a multicast group. These four nodes communicate with the routers associated with their respective networks through IGMP.

## Slide 7: IGMP Operation
R
R
R
Wide Area
Multicast
Routing
Membership_query (periodic)
Membership_report
Leave_group (optional)
Notes: IGMP operation involves the exchange of three types of messages. All these messages are contained within an IP packet.
The first message is membership_query that is sent is sent periodically by a router on its associated network(s). This message is broadcast, i.e., all nodes in the network are the recipients of this message. On receiving this query message, all nodes that are interested in receiving multicast messages respond with their membership_report messages. A membership_report message contains the list of multicast groups to which the sender belongs. A router can also send a specific membership_query message in which it lists a specific group address. Only nodes that belong to that group respond to such a message with their membership_report.
Nodes can send their membership_report without waiting for a query, when they join a particular multicast group.
The third message is the leave_group message which a node sends to a router when it leaves the group. This is an optional message. So, a node may leave the group and not send the leave_group message. Wouldn’t this result in the associated router maintaining outdated group membership information? The answer is no. Note that a node’s membership_report, announcing its membership of a certain group, has a finite lifetime, which is periodically refreshed in response to a query. Consider a node that has left a group X, but has not sent a corresponding leave_group message. When this node receives a memership_query, its response (if there is one at all) does not list X as a group to which it belongs. Consequently, the router’s information about X’s membership to the group ages and is flushed. This is an example of soft-state maintenance and is useful if there is abrupt failure or disconnection of nodes from the network (before they had an opportunity to send the leave_group message).

## Slide 8: Multicast Routing Approaches
Group-shared tree approach:
  Single tree including all edge routers that connect to members of multicast group.
  Multicast messages forwarded along this tree.
Source-based tree approach:
  Separate tree for every source.
  Multicast messages from source sent along tree rooted at the source.
What are the relative advantages of the two approaches?
Notes: As stated earlier, flooding or unicasting to each group member are not viable solutions for multicasting. Multicasting is accomplished by constructing a tree spanning the routers attached to all networks that contain members of the multicast group. If the multicast message can be propagated along this tree to these routers, the routers can in turn deliver the message to the group members.
Two different types of trees can be employed for multicasting. In the group-shared tree approach a single tree is maintained for a group. The multicast message from the source is routed to a router that belongs to the tree (more details in following slides). From there the message is forwarded along the tree to all group members.
In the source-based tree approach there is a separate tree rooted at each source for a group, and messages are propagated along this tree. As the tree is source-specific, it can be optimized for that source.
The source-based trees yield better paths to the destinations, compared to the group-shared tree approach. However, the state maintenance overheads are also higher. If a router lies on a group-shared tree all it needs to maintain is the identity of the group, and its interfaces leading to branches of the tree. If a router is part of source-based trees for N sources multicasting messages to a given group, it needs to maintain the corresponding information for each of those N trees. This poses a serious scalability problem.
On the other hand, if there is cumulatively a heavy volume of multicast traffic (with each source contributing a moderate amount of traffic), the group-shared tree will experience congestion. The source-based tree approach will most likely perform better in such situations as the traffic is distributed across different trees.

## Slide 9: Core-Based Tree (CBT): Group-Shared Approach
Join: unicast join message towards core node.
  Graft every router and link to the tree on the way to the existing tree.
Message Send: unicast message towards core.
  On hitting the tree, at every router, send along all tree links except one on which message was received.
How should the core be selected?
What about optimality of multicast forwarding?
Notes: The Core-Based Tree approach is an example of group shared approach. A specific router is identified as the core router for the group. All nodes that wish to join the group send a unicast join message to the core. The unicast message is forwarded based on the routing table entries at the intermediate nodes. The message is forwarded until it either reaches the core, or hits a router that is already part of the core-based tree (whichever happens first). All the routers and links traversed by the message get added to the core-based tree. In this fashion, with the successive joining of group members the tree grows.
This approach yields a single tree for the group, rooted at the core. Assuming that routes are symmetric (i.e., route from A to B is the same as the route from B to A) and the routing protocol is designed to discover minimum-cost paths, the tree consists of minimum-cost paths from the core to the group members.
A node that wishes to send messages to a multicast group unicasts it towards the core. The message is forwarded until it hits the tree. From that point onwards, the message is propagated by all the routers of the tree along all the branches of the tree (except the one on which the message was received).
The minimum-cost path from the core to a multicast group member is not necessarily the minimum-cost path from the source of the multicast message to that group member. So, the core-based tree approach does not necessarily result in optimal forwarding of multicast messages.

## Slide 10: Core-Based Tree: Node Join
A
B
C
D
F
E
H
G
I
J
L
K
Join
Join
Join
Join
Notes: This figure illustrates the formation of a core-based tree. Router B is the core router. Let, routers A, B, C, F, G and H already be on the tree. When E wishes to join the tree, it generates a join message that is unicast towards the core, B. The unicast messages passes through D to reach H, which is already part of the tree. So, the join message stops at H and all routers and links from E to H (E-D-H) are grafted to the tree.
Then, node J unicasts a join message to B. This message passes through I to reach H, where it stops. So, the segment H-I-J is grafted to the tree. When K unicasts a join message to B, it hits the core-based tree at I. So, the segment K-I is grafted to the tree. Finally, when L wishes to join the multicast group, the segment L-K is grafted to the tree.

## Slide 11: Core-Based Tree: Message Propagation
A
B
C
D
F
E
H
G
I
J
L
K
M
Message
Notes: In this example, node M, which is not a member of the group wishes to multicast a message to the group. So, it unicasts a message towards B. Node D happens to be the first tree node on the path from M to B. So, when the message reaches D, D forwards it along all its tree branches (towards E and H). As E has no other interface to the tree, E does not forward the message. However, H forwards the message along its two other interfaces that correspond to tree branches: towards B and I. From B the message is forwarded to A, C, F and G. From I the message is forwarded to J and K. K then forwards the message to L.

## Slide 12: Reverse Path Flooding: Source-Based Tree Approach
Distance-vector based approach.
Packet arrives at router R with source address S:
If incoming link is on shortest path to S:
  Forward packet along all other incident links.
Otherwise:
  Discard packet.
Consequence: Ensures shortest path propagation along the network.
Notes: In the following slides we will successively refine a solution for the source-based tree approach. We will start with the simplest version, based on the reverse path forwarding, that results in a flooding of the message. The ultimate goal is to construct a tree that contains the shortest paths from the source to the group members. There could be multiple paths between the message source and a router. If paths are symmetric, the shortest path from a router to the source should also be the shortest path from the source to that router (just reverse the sequence of routers on the path).
As the aim is to forward packets only along the shortest route from the source to destinations, a router should forward a multicast packet only if it is received from a neighbor that is the next hop on the router’s path to the source. Multicast packets received by the router from neighbors that are not on the preferred path to the source are ignored.
By employing this approach the multicast message is flooded to all the routers in the network. Then, the routers that are attached to networks with group members (information gathered by the routers through IGMP) can forward the message to the destinations.
This solution is attractive because no router has to maintain state information, beyond what is already in its unicast routing table, to flood a message along the shortest-path tree rooted at the source.

## Slide 13: Reverse Path Flooding
A
S
C
D
F
E
H
G
I
J
L
K
M
Messages that do not
convey new information
Notes: This figure illustrates flooding of a multicast message originated by source S. Rightaway, two problems become apparent:
Routers I, J, K, and L are not interested in receiving the multicast message because there are no multicast group members in that part of the network. Yet, the message gets flooded to them.
There are several links that carry the same message multiple times, once for each incident router that receives the message along its preferred path to the source. For example, both E and M receive the message from D which is the next hop on both their paths to S. So, E forwards the message on its other link that is shares with M. M, also forwards the message along its two other tree links to E and J. Thus, the link EM carries two copies of the message. If there were multicast group members on the link EM, one of these two messages would have served the purpose.

## Slide 14: Drawbacks of Reverse Path Flooding (1)
Multiple transmissions along shared links.
Solution: Reverse Path Broadcast w.r.t. S.
  S is the parent of all links incident on it.
  For all other links: router with minimum distance to S is parent.
  Use router address to break ties.
  Router forwards packets only along child links for S.
Notes: Here we discuss a solution to the second problem discussed in the previous slide. With respect to a given source, each link has a parent router. A link’s parent router is the one that has the best path to the source. If there is a tie among multiple routers attached to a link, the tie is broken using router addresses. When a router receives multicast packets from a source S, along the shortest path to the source, the router forwards the message only if it is the parent of the link.
As each link has exactly one parent, and all the parents are reachable from the source, the message is still propagated along all the links. However, each link sees only one copy of the message. In order to achieve this reduction in communication each router has to maintain a list of its child links with respect to each source.

## Slide 15: Reverse Path Broadcast
A
S
C
D
F
E
H
G
I
J
L
K
M
Notes: The optimization discussed in the previous slide is illustrated here. Source S is the parent of all links incident on it. Consider link A-F. Both A and F are at the same distance from S. So, the tie is broken in favor of the node with the lower identity. Thus, A becomes the parent of the link A-F and transmits the message on the link, but F does not.
Consider link H-D. The two routers connected to the link are H and D, at a distance of 1 and 2, respectively to the source (we assume distance is equal to hop-count). So, router H is the parent of the link and forwards the message on it, while D does not. Similarly, E is the parent of the link E-M, J is the parent of the link J-M, and K is the parent of the link K-L. In each of these three cases the two routers have equal cost paths to the source, and the ties are broken based on router identity.

## Slide 16: Drawbacks of Reverse Path Broadcast
Propagation of messages to routers that are not connected to any multicast group member.
Solution: Pruning, resulting in Reverse Path Multicast.
  Leaf link: a child link that is not on shortest path from any router to source S (e.g. KL).
  If all child links of a router are leaves with no group members:
    Send non-membership report (NMR or prune) to next-hop router for S.
  If NMRs received from all routers on child links, and no group member on child links:
    Send NMR to next-hop router for S.
Notes: We still have the problem of the message propagating to portions of the network that do not contain any members of the multicast group. This problem is solved by pruning portions of the broadcast tree.
First, let us try to understand the meaning of a leaf link for a source-based tree. Let a link L be the child of a router R. This implies that only router R can forward multicast messages, from source S, along L. If this link is not on the shortest path from any router to the source, then this link does not connect any router to its predecessor in the broadcast tree. This means that the only group members that R can reach (either directly or transitively) by transmitting a message on this child link are those that are directly connected to the link. Consequently, if a leaf link does not have any members of the multicast group, there is no point in transmitting a message on that link.
If all child links of a router are leaves with no group members, then the router has no use for the multicast message because the router cannot propagate the multicast message to any group member. So, the router sends a non-membership report (also called a “prune”) message to its next hop router for S, which also happens to be its predecessor in the broadcast tree rooted at S.
Let a router receive prune messages from all routers connected to its child links, and also knows that no group member are connected to its child links. Then the router infers that the subtree rooted at itself contains no group members. So, this router, too, has no use for the multicast message, and sends the prune message to its predecessor in the tree.
In this fashion, portions of the network that do not contain any group members can be pruned from the broadcast tree, and will not have to carry the multicast messages.

## Slide 17: Reverse Path Multicast
A
S
C
D
F
E
H
G
I
J
L
K
M
Prune
Leaf link
of J
Leaf link
of K
Prune
Prune
Prune
Notes: This figure illustrates the pruning of a broadcast tree. Router L has no child link, nor is it a member of the multicast group. So, L sends a prune message to its predecessor I. Router K has one child link, K-L, which is not on the shortest path from any router to S. Hence, link K-L is a leaf link. No node on link K-L is a member of the group. So, K, too, sends a prune message to its predecessor I. Router J has one child link, J-M, which is a leaf and no node on that link is a member of the multicast group. Hence, J also sends a prune message to its predecessor I.
Router I has three child links (I-J, I-K, and I-L). It has received prune messages from all routers along these child links, and no group members are connected to these links. So, I sends a prune message to its predecessor H. Henceforth, H will not forward multicast messages from S along its child link H-I. Consequently, routers I, J, K, and L and all nodes connected to links incident on these routers do not receive the multicast messages.
Combining the two optimizations, namely (i) forwarding of messages only along child links, and (ii) pruning portions of the network with no group members, we have reverse path multicast.

## Slide 18: Distance-Vector Multicast Routing Protocol (DVMRP)
Employs Reverse Path Multicast.
Links pruned by NMR rejoin after Tmaxage (about 2 hours).
Subsequent transmissions for (S,G) would be broadcast.
If additional traffic for same (S,G) pair:
  NMR’s may be triggered once again.
Routers send cancel_NMR messages when downstream nodes join group G.
Notes: The Distance-Vector Multicast Routing Protocol (DVMRP) is based on reverse path multicast. Some enhancements have been made to reduce the amount of state information maintained by routers.
In reverse path multicast, each router needs to maintain some state information. Each time a link is pruned from the multicast tree for a (source, group) pair, its parent needs to maintain information about the pruning so that messages are not forwarded along that link. In addition, for each (source, group) pair a router needs to maintain information about the child links.
Some (source, group) pairs may not be active, i.e., the source may not send any message to the group for an extended period of time. It would not be efficient to maintain state information for inactive (source, group) pairs. Hence, the prune messages in DVMRP are effective for a maximum of two hours. After that the parent node discards information about the pruning. If the (source, group) pair is still active, or becomes active after the pruned link is restored, the next multicast message is sent along the link, and triggers yet another pruning.
If a node on a pruned link joins group G, it can send a cancel_NMR message towards the source. All the routers and links traversed by this message until it hits a router on the source-based tree are grafted to the tree.

## Slide 19: Protocol Independent Multicast (PIM)
Group-shared trees (as in CBT) suitable for large number of low data rate sources.
Source-based trees better suited for high data rate sources.
Periodic broadcasts and pruning incur high overheads for source-based trees.
PIM designed to:
  Use unicast routing tables independent of how they are computed.
  Avoid broadcasting and pruning for sparse groups.
Notes: Group-shared tree does not guarantee optimal paths from each source to members of a multicast group. If the volume of traffic from the source is low, the suboptimality of paths taken by the mluticast packets is not a serious concern. However, if the volume of traffic from a given source is high, it is advisable to forward this traffic to the group members along optimum paths. Hence, source-based trees are preferable for such sources.
Protocol Independent Multicast offers the flexibility to adapt to traffic volume and to the density of destinations. It does not rely on a specific unicast routing protocol. Instead, it uses the information provided by any underlying routing protocol. Hence, it is said to be protocol independent. There are two modes of PIM: PIM-Dense Mode, and PIM-Sparse Mode. If a large number of nodes are members of the multicast group, such that the message has to be forwarded to most of the routers, it may not be worthwhile incurring the cost of constructing and maintaining a multicast tree. On the other hand, if the group members are sparsely distributed, it may be advisable to construct a multicast tree so that the multicast messages are not unnecessarily sent to those portions of the network that have no group members.

## Slide 20: PIM-Dense Mode
Suitable when receivers present in sufficiently large number of subnetworks (dense).
  Not necessary to construct a tree.
Similar to DVMRP.
Prune state held for about 3 minutes.
Similar scaling problems as DVMRP:
  Periodically data gets flooded.
  Routers must keep track of all (source, group) pairs.
Notes: In DVMRP prune state is held in routers for two hours. This requires that prune messages should not be sent in error. Otherwise, some group members may not receive multicast packets for extended periods of time. In order to minimize the impact of erroneous prune messages, PIM-Dense Mode holds prune state information only for about three minutes. This means that every few minutes multicast packets get flooded throughout the network, and that routers need to maintain state information about (source, group) pairs. Hence, this protocol may not be suitable for very large networks.

## Slide 21: PIM-Sparse Mode
Employs core-based tree approach.
Rendezvous Point (RP): equivalent to core.
  RP specific to group.
Destinations send explicit join and leave messages to RP.
Initial join message is wildcarded: applies to all sources.
Sources using group-shared tree tunnel their packets to RP for delivery on that tree.
Let routers feel that volume of traffic from source S, for group G, is high:
  Routers can join a source-based tree for (S,G).
Notes: If multicast group members are located in only a small subset of links, it is not advisable to periodically flood the message along all the links. Hence, PIM-Sparse Mode employs the core-based tree approach. The core router is referred to as a Rendezvous Point. For sources that inject a high volume of multicast traffic, a source-based tree is formed. This ensures that multicast packets from this source travel along the shortest-path to all the destinations.
Unlike core-based tree, the links of group-shared tree in PIM-sparse mode are unidirectional, i.e., they carry multicast packets in only one direction. When a source wishes to multicast a message using this tree, it tunnels the message to the Rendezvous Point. From there the message is propagated along the group-shared tree.
If some sources are generating a large volume of multicast traffic, it is not necessary for them to use the group-shared tree. Instead, the group members can directly send join messages to such sources, forming a source-based tree rooted at that source.

## Slide 22: PIM Spare Mode: Optimization
A
S1
C
RP
F
S2
H
G
I
J
L
K
M
Join
Join
Notes: There are two sources: S1 and S2. Nodes J and K are two destinations. Initially, both of them send join messages towards the Rendezvous Point (RP). This forms a group-shared tree. Subsequently, the two destinations receive multicast packets in the following fashion:
The multicast sources, S1 and S2, tunnel their multicast packets to RP.
RP forwards the packets to J and K.
At a later time, both J and K realize that they are receiving a high volume of multicast traffic originated by S1. So, rather than receiving such packets via RP, along a sub-optimal path, they choose to directly contact S1. K is the first node to send a join message directly towards S1. All routers on the path between K and S1 get grafted onto the source-specific path. Later, when J sends its join message towards S1, the message only propagates until H because all routers between H and S1 have already been grafted onto a source-based tree. Now, when S1 has to send multicast packets it does the following:
Sends a copy of the packets to RP for those group members that may not have joined the source-basedmulticast tree rooted at S1.
Sends the multicast packets to J and K along the source-based multicast tree.
In this example, S2 does not generate a high volume of multicast traffic. So, J and K do not feel the need to send join messages to S2. As a result, multicast packets from S2 first travel to RP. From there they are forwarded to J and K. This illustrates the point that it is possible for destinations to receive multicast packets from some sources along source-based trees, and from other sources along group-shared trees.

## Slide 23: Exercise
Do group members have to know identities of each other?
Does the sender have to belong to the group?
The IGMP leave_group message is optional. Does this mean that a node that forgets to send a leave_group message, before departing the group, will keep receiving multicast messages for the group for ever?
Why may a group-shared tree approach not be suitable for multicasting when cumulatively there is a very high volume of multicast traffic contributed by multiple sources?
Notes: Answers:
Group members do not have to know the identities of each other. A group member communicates its identity to an attached router through IGMP. These routers do not exchange their information. Hence, no node has information about the full membership of the group.
No. The sender need not be a member of the multicast group. In the group-shared tree approach, the sender only needs to know the identity of the core. In the source-based tree approach, the sender does not even need this information. Using prune messages, it can come to know of its incident links along which it needs to send the message.
Not for ever. Until the next membership_query the attached router thinks that the departed node is still a member of the group and keeps forwarding messages to that node. However, when the router does not receive a membership_report for the group from the departed node, and the membership information about the departed node ages, the attached router stops forwarding multicast messages to that node.
In the group-shared tree approach, multicast messages from all sources are forwarded along the same tree. So, a subset of network edges carry all the multicast traffic, and they can become congested if the cumulative volume of multicast traffic is high. If a source-based tree is constructed, it is possible that trees corresponding to different sources have very little, or no overlap. As a result, multicast traffic gets distributed over a much larger set of links in the case of source-based tree approach, avoiding network congestion.